## Slide 1: Bitreduction Make a VST plugin Downsampling Panning
Ear training for digital audio production
Øyvind Brandtsegg

## Slide 2: Digitizing (Sampling)
0,09983342
0,19866933
0,29552021
0,38941834
0,47942554
0,56464247
0,64421769 …
0,5
0,8
1
0,9
0,6
0,1
-0,4
Analog sound wave
Digital sound, fine resolution
Digital sound, coarse resolution

## Slide 3: Bit reduction
b = bits, n = steps (discrete values)
n=2(b)
  16 bits audio has 65536 steps
  Range = -32768 to +32767
Bitreduction algorithm (we want balanced +/-)
  n=2(b-1) gives number of bipolar steps a=round(a*n)/n
  Gives normalized output
  Allows ”fractional” bits (nonsensical but useful)

## Slide 4: VST plugin from DSP kode
Cabbage: open csd, export as effect
  Save in folder where your DAW expect to find plugins
Windows: same name (.csd og .dll)
OSX: .vst file is a bundle (.csd is inside bundle)
  Enable ad hoc codesign in Settings/Miscellaneous
<Cabbage>
form size(400, 300), caption("MyCoolPlug"), pluginId("new1")
rslider channel("Volume"), bounds(10, 25, 70, 70),
text("Volume"), range(0, 1, 1, 0.35)
rslider channel("Drive"), bounds(90, 25, 70, 70),
text("Drive"), range(1, 10, 1)
</Cabbage>
<CsOptions>
-n -d
</CsOptions>

## Slide 5: Resampling Upsampling – interpolation - decimation/downsampling
Nyquist, Aliasing, Mirror images
Simplified algorithm: (Downsampling/Decimation)
  Pulse generator at new sample rate
  Sample and hold
  Generous amount of artifacts/aliasing
    ”zero-order hold distortion”
Linear interpolation
  Disregard in-between samples
  Line segment between each sample
Zero padding
  In-between samples = null
  Lowpass filter
http://dspguru.com/dsp/faqs/multirate/resampling
NB: As a processing effect, we downsample but represent the signal in the original sampling rate. This works differently than «real» downsampling.

## Slide 6: Samplerate, Nyquist ?
sr/8
sr/4
sr/2
sr/2

## Slide 7: Aliasing
Zero order hold distortion

## Slide 8: In practice
When should we be especially aware and cautious about aliasing?
  …When processing the audio signal in such a way that we might generate new frequencies, e.g. distortion, modulation, etc.

## Slide 9: Workshop assignment
Explore code examples for bitreduction and resampling
Run offline (terminal: csound bitreduction.csd)
Make VST/AU plugin
  Run in Cabbage
  Export plugin
  Run in DAW